## Slide 1
Pogo: 2-D SLIP hopper, 6 robots incl. 3 outside the DR family - success %, frozen test seed 3301, 3 seeds
arm | real trials / robot | success % [95 % CI] | apex err (cm) | speed err. dv (m/s)
ours, zero-shot | 0 | 7.6 [1.4, 15.3] | 3.81 | 0.102
ours + DistILC stage | 36 | 90.8 [84.2, 96.5] | 0.81 | 0.027
ours+DR, zero-shot | 0 | 48.8 [37.7, 59.7] | 1.61 | 0.090
ours+DR + DistILC stage | 36 | 97.6 [94.8, 99.8] | 0.47 | 0.023
PPO+DR, zero-shot | 0 | 73.6 [62.2, 84.0] | 0.71 | 0.068
PPO+DR + DistILC stage | 36 | 97.2 [94.6, 99.3] | 0.38 | 0.023
PPO fine-tuned on the robot | 48 / 384 | 79.5 / 94.4 | 0.60 / 0.38 | 0.059 / 0.034
FADA (own adaptation) | 24 | 95.1 [91.7, 97.9] | 0.79 | 0.030
RMA, zero-shot (privileged) | 0 | 98.6 [96.5, 100] | 0.34 | 0.020

## Slide 2
Pogo: Ablations of the stage's update direction (validation, nominal start s0, 24 trials)
arm | success %
stage, Gauss-Newton step through the sim Jacobian | 79.7
open-loop Jacobian (no feedback term) | 5.2
flipped Jacobian (the 180-degree direction control) | 0.0
+ trust region / no rollback | 77.1 / 79.7
sim-stage final snapshot instead of the stopping-rule pick | 34.4
Sources: src/ilc_pogo/results_table_test3301.txt (success as scored by common.hop_metrics / ci.py), src/ilc_pogo/NOTES.md (controls). No random-direction arm in this domain; the flipped Jacobian is the direction control.

## Slide 3
Car: F1TENTH 25-degree drift, 8 cars incl. friction x0.9/0.7/0.6 - b25 success %, validation seed 301, 3 seeds
arm | real laps / car | b25 success % (mean +- sd) | crash % | all plans % | test 2701 b25 %
ours, zero-shot | 0 | 40.8 +- 4.0 | 45.8 | 49.9 | 40.1
ours + DistILC ladder stage | 10 | 89.9 +- 14.2 | 1.9 | 94.9 | 91.1
PPO+DR (task reward), zero-shot | 0 | 49.8 +- 9.3 | 28.1 | 55.3 | 48.6
PPO+DR + our ladder stage | 10 | 85.9 +- 1.1 | 7.5 | 86.2 | 85.9
PPO+DR on our rungs (no ILC) | 0 | 79.5 +- 10.0 | 8.3 | 87.0 | 80.0
RMA (task), zero-shot | 0 | 39.1 +- 3.5 | 31.6 | 52.1 | 38.5
RMA + our ladder stage | 10 | 75.2 +- 4.5 | 10.8 | 79.5 | -

## Slide 4
Car: Paired b25 differences (cluster = car x plan, 16 clusters, 95 % bootstrap) and direction ablations
comparison | delta b25 (pts)
ours + ladder - PPO+DR + ladder | +4.0 [-6.8, +16.7]
ours + ladder - RMA + ladder | +14.8 [-1.4, +32.5]
RMA + ladder - RMA zero-shot | +36.1 [+18.1, +54.9]
older setup (mu 0.2, seed 0, 24 laps): stage 79 % / open Jacobian 79 % / flipped Jacobian 51 % | 
Sources: src/ilc_f1tenth/ilc2real/runs/hw/redo_val_table.txt, NOTES.md (success as scored by reeval.py: 12 runs x 5 chained laps). No random-direction arm; the flipped Jacobian is the control.

## Slide 5
Quadruped: Go1 jump to flat/box goals, 4 robots incl. r5: friction 0.59, mass x1.14 - start drB_s2, 36 paired (seed, robot) cells
arm | real jumps / robot | success % | score (raw) | score (capped) | d success vs control (pts) | d capped vs control
zero-shot (start network) | 0 | 43.0 | 21.30 | 12.06 | - | -
DistILC stage (recipe) | 24 | 43.2 | 20.19 | 10.56 | +1.6 [-0.9, +3.9] (n=36) | -1.05 [-1.53, -0.61]
stage, pooled-data variant | 24 | 45.3 | 19.30 | 10.80 | +4.9 [+2.3, +7.3] (n=12) | -0.79 [-1.60, -0.08]
random-direction control | 24 | 41.6 | 20.04 | 11.61 | (control) | (control)

## Slide 6
Quadruped: Replication: start network drCft_s2 (24 paired cells)
arm | real jumps / robot | success % | score (raw) | score (capped) | d success vs control (pts) | d capped vs control
zero-shot (start network) | 0 | 39.8 | 22.00 | 12.26 | - | -
DistILC stage (recipe) | 24 | 44.5 | 20.82 | 11.89 | +7.2 [+2.5, +12.0] (n=24) | -0.97 [-1.44, -0.49]
random-direction control | 24 | 37.4 | 23.10 | 12.86 | (control) | (control)
Validation goals (planeval); success = pre-registered (no fall, |ex| <= 5 cm, |ez| <= 3 cm); score = 0.01 landing cost + 20 fall, lower = better; capped = each jump's cost term capped at 20 (POST HOC: the raw mean is dominated by a few tumbles). r5 alone, recipe - control success: drB +2.8 [+0.0, +5.6] pts (9 cells), drCft -3.6 [-6.8, +0.0] pts (6 cells). Paired 95 % bootstrap CIs.